## Slide 1: HISTOLOGICAL TECHNIQUES
TISSUE PROCESSING- IN ROUTINE HISTOLOGY AND HISTOPATHOLOGY A SPECIMEN IS SLICED IN TO 0.5 CM.
THESE SLICES ARE PROCESSED AND FINALLY FURTHER SECTIONED IN TO 5-7 µm THIN SECTIONS.THESE SECTIONS ARE MOUNTED AND STAINED ON GLASS SLIDES TO MAKE THEM SUITABLE FOR MICROSCOPIC OBSERBATION. THIS ENTIRE PROCEDURE IS CALLED TISSUE PROCESSING.
HISTOLOGICAL TISSUE PROCESSING INVOLVES THE FOLLOWING MAJOR STEPS.

## Slide 2: TISSUE COLLECTION
FOR HISTOLOGICAL STUDIES, SUITABLE TISSUE IS COLLECTED FROM CADAVERS, FORENSIC AUTOPSIES,SURGICAL PROCEDURES,ANIMALS WITH PERMISSION FROM AUTHORITIES(ETHICS AND RESEARCH COMMITTEES).
TISSUES FIXATION- COLLECTED SPECIMEN IS PRESERVED FOR RETAINING THEIR BIOLOGICAL STRUCTURE WITHOUT ANY SIGNIFICANT DISTORTION OR DECOMPOSITION.
10% FORMALIN IS THE MOST COMMONLY USED FIXATIVE.
OTHER FIXATIVES INCLUDE GLUTARALDEHYDE,MERCURIC CHLORIDE etc.

## Slide 3: PARAFFIN BLOCK MAKING
IT IS DIFFICULT TO MAKE THIN SECTIONS OF OF THE TISSUE AS MOST OF THE CELLS CONTAIN WATER(50-60%).HENCE THE TISSUE IS PROCESSED TO REPLACE WATER WITH FIRM MATEREAL(PARAFFIN WAX) AND TO MAKE THE TISSUE SUITABLE FOR CUTTING.
IT INVOLVES THE FOLLOWING STEPS:
DEHYDRATION: TISSUE SLICE IS TREATED WITH ASCENDING GRADES OF ALCOHOLS(50%,70%,90%,AND ABSOLUTE/100%)TO GRADUALLY REMOVE WATER FROM THE TISSUE.
CLEARING- TISSUE SLICE IS TREATED WITH XYLENE(CLEARING AGENT). CLEARING AGENT MAKES THE THE TISSUE CLEAR BY CHANGING THE REFRACTIVE INDEX OF THE TISSUE.

## Slide 4: CONT.
REMOVAL OF CLEARING AGENT- TISSUE SLICE IS KEPT IN MELTED PARAFFIN THAT REPLACES XYLENE BY INFILTRATION IN THE TISSUE.
EMBEDDING- TISSUE SLICE IS KEPT FIXED IN THE MELTED PARAFFIN AND ALLOWED TO FORM A SOLID BLOCK ON COOLING. THIS SOLID BLOCK MAKES THE TISSUE SUITABLE FOR SECTIONING.
TISSUE SECTIONING- MICROTOME IS AN INSTRUMENT USED FOR THIN SECTIONING OF TISSUE. PARAFFIN BLOCK IS FITTED ON MICROTOME AND CUT IN TO THIN SECTIONS(5-7µm).THESE SECTIONS ARE TRANSFERRED TO GLASS SLIDES.

## Slide 5: CONT.
STAINING- A SECTION ON A GLASS SLIDE IS STAINED WITH SUITABLE STAINING. HEMATOXYLIN AND EOSIN ARE COMMONLY USED STAINS.
MOUNTING- STAINED SECTION IS MOUNTED WITH THE HELP OF A COVER SLIP AND DPX(GLUE) TO MAKE READY FOR OBSERVATION UNDER MICROSCOPE AND PRESERVE.
SPCIAL STAINS- MANY STRUCTURES OR SUBSTANCES CAN NOT BE DIFFERENTIATED FROM EACH OTHER WITH THE HELP OF ROUTINE HEMATOXYLININ AND EOSIN STAINING.
FOR THE VISUALIZATION AND DIFFERENTIATION OF SPECIFIC STRUCTURE,SPECIAL STAINS ARE REQUIRED.

## Slide 6: HEMATOXYLIN AND EOSIN STAINING
HEMATOXYLIN AND EOSIN STAIN IS MOST COMMONLY USED IN ROUTIN HISTOLOGY AND HISTOPATHOLOGY.
HEMATOXYLIN IS A BASIC DYE THAT IS OBTAINED FROM WOOD OF HEMATOXYLON CAMPECHIANUM TREE.
HEMATOXYLIN STAINS NUCLEI,CALSIUM DEPOSITS,FIBRIN,MUSCLE CROSS STRIATION,MATRIX IN CARTILAGE etc.
EOSIN IS AN ACIDIC DYE THAT IS DERIVED FROM FLUORESCEIN.
EOSIN STAINS BASIC OR EOSINOPHILIC COMPOUNDS SUCH AS CYTOPLASM,CONNECTIVE TISSUE(COLLAGEN FIBRES),MUSCLE FIBRES,RBC etc.

## Slide 7: STEPS IN H&E STAINING
DEPARAFFINIZE THE SECTION USING XYLINE, REHYDRATE THE SECTION WITH DESCENDING GRADES OF ALCOHOL(100%,90%,70%,AND WATER).STAINING WITH HEMATOXYLIN,REMOVAL OF EXCESS HEMATOXYLIN USING(ACID ALCOHOL, AND WATER WASH/BATH), STAINING WITH EOSIN AND DEHYDRATION. DEHYDRATED SLIDE IS PRESERVED BY FIXING COVERSLIP USING DPX.

## Slide 8: DECALCIFICATION
CALCIFIED TISSUE(BONES) CAN NOT BE SECTIONED PROPERLY USING ROUTINE MICROTOME.
DECALCIFICATION IS THE TECHNIQUE USEFUL FOR REMOVING DEPOSITED MINERALS FROM THE MATRIX OF THE TISSUE TO FACILITATE MICROTOME SECTIONING.
THE FOLLOWING AGENTS ARE USEFUL FOR REMOVING MINERAL ACIDS(NITRIC ACID,HYDROCHLORIC ACID), WEAK ORGANIC ACIDS(FORMIC ACIDS) AND CALSIUM CHELATING AGENT (EDTA).